ARCHITECTURAL SPECIFICATIONS FOR

ENCORE™ SERIES 3 ACOUSTICAL WOOD

WALL AND CEILING PANELS

[Project Name]

[Project Location]

PART 1 — GENERAL

1.1 Description of Work:

- Work Included: Provide Architectural Components Group, Inc. Encore™ Series 3 EN3 acoustical wood ceiling and wall panel system where shown on architectural drawings, and as specified in this specification.

1.2 Quality Assurance:

- Architectural Components Group, Inc. Encore™ Series 3 ceiling and wall system for this project shall maintain the quality as instituted by the architect or A.W.I.

- Design Criteria: Manufacture of Encore™ EN3-xxxx-H5 ceiling and wall system shall be installed true and plumb to within manufacturing tolerance of 1/8” within 8’ of length.

- Product Construction: Wood shall be kiln dried to 10%. Cracking, checking and warpage of members will not be acceptable.

1.3 Submittals:

- Technical Data: Submit manufacturer’s data and installation instructions.

- Shop Drawings: Submit 4 copies of shop drawings showing all areas involved, attachment conditions and perimeter circumstances.

- Submittal Sample: Submit 1 product sample for approval by architect.

1.4 Delivery, Storage and Handling

- Material must be stored and installed only in secured ambient environment (humidity min. 25% - max. 55%, temperature not to exceed 86 degrees).

- Windows, doors and all wet-work must be completed before unpacking and installation. Handle carefully to avoid damage.

PART 2 — PRODUCTS

2.1 Acceptable Manufacturer

Architectural Components Group, Inc., 521 George Street, Marshfield, MO 65706
Phone (417) 869-6777	Fax (417) 869-7888

2.2 Product Type

- Product: Encore™ Series 3 acoustical wood system shall be product: EN3-xxxx-x-x

Nomenclature for: EN3-4896-I5

EN3 = Encore™ Series 3

4896 = a panel 48” wide x 96” length

I = 1-1/2” thick

5 = face grooves 5mm O.C.

- Size: Encore™ Series 3 panels shall be up to 5’ wide x 12’ length [limited by veneer length] by x” thick.

- Face Profile: Face grooves shall be 5, 8, 10, 12, 16 or 25mm on center.

- Specie: System shall consist of specie wood veneer [e.g., quartered, slip-matched cherry veneer].

- Finish: Finish shall utilize ACGI clear finish with satin sheen or specify custom stain to match architect sample.

- Insulation: Encore™ Series 3 panels shall be manufactured with encapsulated insulation, nominal 1” thick.

- Panel Edges: Raw or edge banded with matching veneer as required.

- Core: The substrate material shall or shall not be manufactured with no added urea formaldehyde.

- Certification: The wood veneer shall or shall not be FSC. The substrate shall or shall not be FSC. If FSC, the Chain of Custody certificate shall or shall not be provided.

- Fire Rating: Wood components shall achieve a Class I(A) or Class III(C) fire rating.

- Attachment System: Encore™ Series 3 wall system shall be mounted according to manufacturers suggested method of suspension. This system shall comply with Seismic Zone 2-4 regulations as required.

PART 3 — EXECUTION

3.1 Installation

- The Encore™ ceiling and wall system shall be handled and installed with care in order to prevent surface and structure damage. Field cutting shall be kept to a minimum and performed as recommended by manufacturer.

- The contractor shall measure ceiling and/or wall areas to establish layout for hangers and carriers, in accordance with installation instructions.

- Ceiling panels shall be suspended using ACGI FP1, FP2, FP3, FP4, FP5 or FP6 mounting methods.

- The ceiling panel suspension system shall be suspended by 15/16” HD T-grid with main runners on 2’ centers and cross T’s every 2’ or “Unistrut” (supporting members are a contractor supplied item and shall be suspended according to architect’s drawings and manufacturers’ shop drawings).

- Contractor shall clean all panels prior to installation according to manufacturer’s recommended maintenance procedures. Upon completion of installation, panels shall be inspected and cleaned as needed.

PART 4 — WARRANTY

4.1 Product Warranty

- Architectural Components Group, Inc. shall warranty the Encore™ acoustical wood panel system against manufacturer’s defects up to one year. Changes in finish or dimensions due to ultra violet light, excessive temperature or humidity conditions and/or abuse of any kind shall void any warranties from ACGI.

- Install conditions for the area should remain for the proper occupied conditions of humidity and temperature (humidity min. 25% - max. 55%, temperature not to exceed 86 degrees).

- The contractor shall warranty for one year all work from final acceptance of completed work.

# Text boxes

Architectural Components Group, Inc.

521 George St.

Marshfield, MO 65706

417-869-6777  /  417-869-7888 fax

info@acgiwood.com / acgiwood.com