Architectural Components Group, Inc.

521 George St.

Marshfield, MO 65706

417-869-6777  /  417-869-7888 fax

info@acgiwood.com / acgiwood.com

ARCHITECTURAL SPECIFICATIONS FOR

LINEAR OPEN SERIES 3

PANELIZED WOOD WALL & CEILING SYSTEM

[Project Name]

[Project Location]

PART 1 — GENERAL

1.1 Description of Work:

- Work Included: Provide Architectural Components Group, Inc. Linear Open Series 3 LO3 panelized wood wall & ceiling system where shown on architectural drawings, and as specified in this specification.

1.2 Quality Assurance:

- Architectural Components Group, Inc. LO3-xxxx-C Linear Open panelized wall & ceiling system for this project shall maintain the quality as instituted by the architect or A.W.I.

- Design Criteria: Manufacture of Linear Open panelized wall & ceiling system LO3-xxxx-C shall be installed true and plumb to within manufacturing tolerance of 1/8” within 8’ of length.

- Product Construction: Wood shall be kiln dried to 10%. Cracking, checking and warpage of members will not be acceptable.

1.3 Submittals:

- Technical Data: Submit manufacturer’s data and installation instructions.

- Shop Drawings: Submit 4 copies of shop drawings showing all areas involved, attachment conditions and perimeter circumstances.

- Submittal Sample: Submit 1 product sample for approval by architect.

1.4 DELIVERY, STORAGE AND HANDLING

- Material must be stored and installed only in secured ambient environment (humidity min. 25% - max. 55%, temperature not to exceed 86 degrees).

- Windows, doors and all wet-work must be completed before unpacking and installation. Handle carefully to avoid damage.

PART 2 — PRODUCTS

2.1 Acceptable Manufacturer:

Architectural Components Group, Inc., 521 George Street, Marshfield, MO 65706 Phone (417) 869-6777	Fax (417) 869-7888

2.2 Product Type

- Product Configuration: Linear Open Series 3 wood panelized system: LO3-xxxx-C

Nomenclature for product LO3-325-C:

LO3 = Linear Open Series 3

325 = 3-1/4” wide

C = 3/4” thick plank

- Wood planks shall be provided in a size of: ___” wide x 3/4” thick.

- Panels shall be factory assembled with wood planks connected with black, rectangular, wood backers.

- Panel width shall be [1’ and/or 2’ wide]. Panel length shall be 8’ and/or 10’ length (if veneer) or 2’ up to 10’ length in 1’ increments (if solid wood).

- Wood planks shall be installed with a 3/4" reveal between planks. Linear wood members shall be ___” module size (with the module size equal to wood plank width ___” plus 3/4” reveal); [e.g., product # LO3-325-C has a 3-1/4” wide plank plus a 3/4” reveal that equals a 4” module].

- Optional black non-woven felt shall or shall not be factory attached behind the reveal of each plank.

- Wood Specie: System shall consist of desired solid wood or veneer; wood specie. If veneer, it shall have matching veneer edge banding on both long sides.

- Finish: Wood finish shall utilize ACGI clear finish with satin sheen or specify stain to match architect sample. Back of planks shall be factory sealed.

- Certification: If solid wood, wood shall or shall not be FSC certified. If wood veneer, wood veneer shall or shall not be FSC certified, and the core material shall or shall not be FSC certified. If FSC, Chain of Custody shall or shall not be provided.

- NAUF: If veneer, substrate material shall or shall not be manufactured with no added urea formaldehyde.

- Fire Rating: Panels shall achieve a Class I(A) or Class III(C) Fire Rating.

- Normal installation is with an open reveal between planks, with a contractor-supplied black-face insulation installed above the planks.

- Attachment System: Linear Wood Wall and Ceiling System shall be suspended according to manufacturer’s suggested method of suspension as per the design details provided in the plans.

PART 3 — EXECUTION

3.1 Installation

- Linear Wood Ceiling System shall be handled and installed with care in order to prevent surface and structure damage. Field cutting shall be kept to a minimum and performed as recommended by manufacturer.

- The contractor shall suspend planks in accordance with manufacturer’s recommended installation guides and shop drawings.

- The ceiling system shall be suspended by 15/16” black HD T-Grid with main runners on 2’ centers and cross T’s every 4’.

- Panels shall be installed by screwing through the wood backer into the T-Grid and attaching the panels in accordance to the manufactures’ installation instructions.

- Contractor shall clean all panels prior to installation according to manufacturer’s recommended maintenance procedures. Upon completion of installation, panels shall be inspected and cleaned as needed.

PART 4 — WARRANTY

4.1 Product Warranty

- Architectural Components Group, Inc. shall warranty the Linear wood wall & ceiling system against manufacturer’s defects up to one year. Changes in finish or dimensions due to ultra violet light, excessive temperature or humidity conditions and/or abuse of any kind shall void any warranties from ACGI.

- Install conditions for the area should remain for the proper occupied conditions of humidity and temperature (humidity min. 25% - max. 55%, temperature not to exceed 86 degrees).

- The contractor shall warranty for one year all work from final acceptance of completed work.